## Slide 1: 并行程序设计
任课教师：黄聃（Huang，Dan）

## Slide 2
Data-Level Parallelism in Vector, SIMD, and GPU Architectures (Chapter 4)
Based on the slides of Computer Architecture, a Quantitative Approach, 6th Edition.
2

## Slide 3
Data-Level Parallelism in Vector, SIMD, and GPU Architectures (Chapter 4)
Based on the slides of Computer Architecture, a Quantitative Approach, 6th Edition.
3

## Slide 4: Contents
4
SIMD architecture
Vector architectures optimizations: Multiple Lanes, Vector Length Registers, Vector Mask Registers, Memory Banks, Stride, Scatter-Gather,
Programming Vector Architectures
SIMD extensions for media apps
GPUs – Graphical Processing Units
Fermi architecture innovations
Examples of loop-level parallelism
Fallacies

## Slide 5: Flynn's Taxonomy
SISD - Single instruction stream, single data stream
SIMD - Single instruction stream, multiple data streams
  Extend pipelined execution of many data operations, superscalar
  Simultaneous parallel data operations in most instruction set. E.g. SSE( streaming SIMD extensions), AVX
  New: SIMT – Single Instruction Multiple Threads (for GPUs)
MISD - Multiple instruction streams, single data stream
  No commercial implementation
MIMD - Multiple instruction streams, multiple data streams
  Tightly-coupled MIMD (shared memory, NUMAs), OpenMP and Pthreads
  Loosely-coupled MIMD (distributed memory system, e.g. cluster), MPI
Classes of Computers
5

## Slide 6: Advantages of SIMD architectures
Can exploit significant data-level parallelism for:
  A set of applications has significant data-level parallelism
Matrix-oriented scientific computing
Media-oriented image and sound processors
Tensor-oriented AI applications (training, inference)
More energy efficient than MIMD
1. Only needs to fetch one instruction per multiple data operations, rather than one instr. per data op.
2. Makes SIMD attractive for personal mobile devices
Allows programmers to continue thinking sequentially
Introduction
6

## Slide 7: SIMD parallelism
SIMD architectures
  A. Vector architectures, extends pipelined execution (SI) of many data operations (MD).
    SIMD extensions for mobile systems and multimedia applications, multimedia extensions (MMX) in 1996, streaming SIMD extensions (SSE), advanced vector extensions (AVX)
  B. Graphics Processor Units (SIMT, GPUs)
Introduction
7

## Slide 8
6
Figure 4.1 Potential speedup via parallelism from MIMD, SIMD, and both MIMD and SIMD over time for x86 computers. This figure assumes that two cores per chip for MIMD will be added every two years and the number of operations for SIMD will double every four years.
SIMD/MIMD comparison. Potential speedup for SIMD twice that from MIMD!
  x86 multicore processors  expect two additional cores per chip per year
  SIMD  width to double every four years

## Slide 9: A. Vector architectures
Basic idea:
  Read sets of data elements into “vector registers”
  Operate on those registers
  Disperse the results back into memory
  A single instruction works on vectors of data, which results in dozens of register-register operations on independent data elements.
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth
  Reason: vector loads and stores are deeply pipelined and overlapped with computations, the program endeavors to pay the long memory latency only once per vector load or store, rather than once per element, thus amortizing the latency, e.g., 32 elements.
  Overall, vector programs strive to keep the memory busy.
Vector Architectures
9
Target on memory wall challenges

## Slide 10: Cray-1 (1976)
RISC vector instruction set extension

## Slide 11: Example of vector architecture
RV64V  RV64G, RV64V extended RV64G with vector instructions, here RV (RISC-V)
  RISC-V (pronounced "risk-five") is an open standard instruction set architecture (ISA) based on established reduced instruction set computer (RISC) principles.
Vector registers
  Each register holds a 32-element, 64 bits/element vector
  Register file has 16 read ports and 8 write ports, A register file is an array of processor registers in a central processing unit (CPU).
Vector functional units – FP add and multiply
  Fully pipelined
  Data and control hazards are detected
Vector load-store unit
  Fully pipelined
  One word per clock cycle after initial latency
Scalar registers
  31 general-purpose registers
  32 floating-point registers
  Provide data as input to the vector functional units
  Compute addresses to pass to the vector load/store unit
Vector Architectures
11

## Slide 12
9
Figure 4.2 The basic structure of a vector architecture, RV64V, which includes a RISC-V scalar architecture. There are also 32 vector registers, and all the functional units are vector functional units. The vector and scalar registers have a significant number of read and write ports to allow multiple simultaneous vector operations. A set of crossbar switches (thick gray lines) connects these ports to the inputs and outputs of the vector functional units.

## Slide 13: Cray-1 (1976)
Vector Architectures
13
Single Port
Memory
16 banks of 64-bit words
+
8-bit SECDED单错纠正双错检测
80MW/sec data load/store
320MW/sec instruction
buffer refill
4 Instruction Buffers
64-bitx16
NIP
LIP
CIP
(A0)
( (Ah) + j k m )
64
T Regs
(A0)
( (Ah) + j k m )
64
B Regs
S0
S1
S2
S3
S4
S5
S6
S7
A0
A1
A2
A3
A4
A5
A6
A7
Si
Tjk
Ai
Bjk
FP Add
FP Mul
FP Recip
Int Add
Int Logic
Int Shift
Pop Cnt
Sj
Si
Sk
Addr Add
Addr Mul
Aj
Ai
Ak
memory bank cycle 50 ns processor cycle 12.5 ns (80MHz)
V0
V1
V2
V3
V4
V5
V6
V7
Vk
Vj
Vi
V. Mask
V. Length
64 Element Vector Registers
Novel design

## Slide 14: Vector Arithmetic Execution
Use deep pipeline to execute element operations
Simplify control of deep pipeline, since elements in vector are more independent and consistent, compared to general instruction pipelines.
Six stage
Multiply
pipeline

## Slide 15
Vector Memory System
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator
Cray-1, 16 banks, 4 cycle bank busy time, 12 start-up cycle latency
  Bank busy time: Cycles between accesses to same bank
  Start-up cycle latency: Cycles to access the first byte on a memory bank
Memory bus
about 1 cycle

## Slide 16: RV64V instructions
vadd : add two vectors.
vld/vst: vector load and vector store from address
  x5  the address of vector X
  x6  the address of vector Y
Example: DAXPY (double precision a*X+Y)  6 instructions
Assumption: the vector length matches the number of vector operations – no loop necessary.
Vector Architectures
vsetdcfg 4*FP64 # Enable 4 DP FP vregs
fld f0,a # Load scalar a
vld v0,x5 # Load vector X
vmul v1,v0,f0 # Vector-scalar mult
vld v2,x6 # Load vector Y
vadd v3,v1,v2 # Vector-vector add
vst v3,x6 # Store the sum
vdisable # Disable vector regs

## Slide 17: DAXPY using RV64G instructions
Example: DAXPY (double precision a*X+Y)
Requires almost 258 RV64G ops when the vectors have 32 elements 32 elements of a vector, 8 ops
Vector Architectures
fld f0,a # Load scalar a
addi x28,x5, #256 # Last address to load
Loop: fld f1,0(x5) # Load X[i]
fmul.d f1,f1,f0 # a * X[i]
fld f2,0(x6) # Load Y[i]
fadd.d f2,f2,f1 # a * X[i] + Y[i]
fsd f2,0(x6) # Store into Y[i]
addi x5,x5,#8 # Increment index to X
addi x6,x6,#8 # Increment index to Y
bne x28,x5,Loop # Check if done
258=2+32*8

## Slide 18: Execution time – pipelined vector instructions
How to quantify the run time of vector instructions.
  E.g. vld-> vmul -> vadd
Vector Architectures
Load
Mul
Add
Load
Mul
Add
Time
Time
Or
Expected pipelined execution.
However there are hazards to avoid

## Slide 19: Execution time – pipelined vector instructions
Pipelined vector execution time depends on:
  Length of operand vectors
  Structural hazards (结构风险), A structural hazard occurs when two (or more) instructions that are already in pipeline need the same resource, e.g. conflicts on memory controller
  Data dependencies
RV64V functional unit consumes one element per clock cycle
 Execution time is approximately the vector length
Convoy （护航指令组）  Set of vector instructions without structural hazards that could potentially execute together, how to take advantage of pipeline?
  No structural hazards, if have, the instructions must be serialized and initiated in different convoy
Vector Architectures

## Slide 20: Chaining and chimes
Chaining （链接操作）
  Allows a vector operation to start as soon as the individual elements of its vector source operand become available
Chime （钟鸣，计时单位）
  Unit of time to execute one convey
  Assuming processing one element consuming one clock
    m conveys executes in m chimes
    For vector length of n, requires m x n clock cycles
    Ignore the start-up time, that is the latency in clock cycles until the pipeline is full.
    The chime ignores some processor-specific overheads, many of which are dependent on vector length.
Sequences with read-after-write dependency hazards can be in the same convey via chaining
Vector Architectures

## Slide 21: Vector Chaining
Vector version of register bypassing
  introduced with Cray-1
Memory
V1
Load Unit
Mult.
V2
V3
Chain
Add
V4
V5
Chain
LV v1
MULV v3,v1,v2
ADDV v5, v3, v4

## Slide 22: Vector Chaining Advantage
With chaining, can start dependent instruction as soon as first result (element) appears
Load
Mul
Add
Load
Mul
Add
Time
Without chaining, must wait for last element of result to be written before starting dependent instruction

## Slide 23: Example – one functional unit
vld v0,x5 # Load vector X
vmul v1,v0,f0 # Vector-scalar multiply
vld v2,x6 # Load vector Y
vadd v3,v1,v2 # Vector-vector add
vst v3,x6 # Store the sum
Three convoys:
For 32 element vectors, requires 32 x 3 = 96 clock cycles
3 chimes (3 clocks per element), 2 FP ops per element,
cycles per FLOP = 96 / (32 * 2) = 1.5
Overheads ignored: 1) vector instruction issue time, 2) vector startup time: the latency in clock cycles until the pipeline is full.
Vector Architectures
1. vld vmul
2. vld vadd
3. vst
vld
vmul
vld
vadd
vst
Time
Chaining
Chaining
3 convoys (护航指令组)
3 chimes (钟鸣)
32 elements

## Slide 24: Cray-1 (1976)
Vector Architectures
24
Single Port
Memory
16 banks of 64-bit words
+
8-bit SECDED单错纠正双错检测
80MW/sec data load/store
320MW/sec instruction
buffer refill
4 Instruction Buffers
64-bitx16
NIP
LIP
CIP
(A0)
( (Ah) + j k m )
64
T Regs
(A0)
( (Ah) + j k m )
64
B Regs
S0
S1
S2
S3
S4
S5
S6
S7
A0
A1
A2
A3
A4
A5
A6
A7
Si
Tjk
Ai
Bjk
FP Add
FP Mul
FP Recip
Int Add
Int Logic
Int Shift
Pop Cnt
Sj
Si
Sk
Addr Add
Addr Mul
Aj
Ai
Ak
memory bank cycle 50 ns processor cycle 12.5 ns (80MHz)
V0
V1
V2
V3
V4
V5
V6
V7
Vk
Vj
Vi
V. Mask
V. Length
64 Element Vector Registers

## Slide 25: Problems motivate optimization on vector processor

## Slide 26: Optimizations
Multiple Lanes （多条车道） processing more than one element per clock cycle
Vector Length Registers （向量长度寄存器） handling non-32 wide vectors
Vector Mask Registers （向量遮罩寄存器） handling IF statements in vector code
Memory Banks （内存组） memory system optimizations to support vector processors
Stride （步幅） handling multi-dimensional arrays
Scatter-Gather （分散-集中） handling sparse matrices
Programming Vector Architectures （向量体系结构编程） program structures affecting performance
Question: how these optimizations map to MPI and OpenMP?

## Slide 27: Optimizations
Multiple Lanes （多条车道） processing more than one element per clock cycle
Vector Length Registers （向量长度寄存器） handling non-32 wide vectors
Vector Mask Registers （向量遮罩寄存器） handling IF statements in vector code
Memory Banks （内存组） memory system optimizations to support vector processors
Stride （步幅） handling multi-dimensional arrays
Scatter-Gather （分散-集中） handling sparse matrices
Programming Vector Architectures （向量体系结构编程） program structures affecting performance
Question: how these optimizations map to MPI and OpenMP?

## Slide 28: 1. A four lane vector unit
w
RV64V instructions only allo element N of one vector to take part in operations involving element N from other vector registers this simplifies the construction of a highly parallel vector unit
  Lane  contains one portion of the vector register elements and one execution pipeline from each functional unit
  Analog with a highway
with multiple lanes!!

## Slide 29: Single versus multiple add pipelines
C= A+B
One versus four additions per
clock cycle
Each pipe adds the corresponding elements of the two vectors
C(i) = A(i) + B(i)

## Slide 30: Vector Instruction Execution
ADDV C,A,B
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units

## Slide 31: Automatic Code Vectorization
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vectorization is a massive compile-time reordering of operation sequencing
 requires extensive loop dependence analysis
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time

## Slide 32: Vector Programming Model
Vector Architectures
32
32
+
+
+
+
+
+
[0]
[1]
[VLR-1]
Vector Arithmetic Instructions
ADDV v3, v1, v2
v3
v2
v1
Scalar Registers
r0
r15
Vector Registers
v0
v15
[0]
[1]
[2]
[VLRMAX-1]
VLR
Vector Length Register
v1
Vector Load and Store Instructions
LV v1, r1, r2
Base, r1
Stride, r2
Memory
Vector Register

## Slide 33: Optimizations
Multiple Lanes （多条车道） processing more than one element per clock cycle
Vector Length Registers （向量长度寄存器） handling non-32 wide vectors
Vector Mask Registers （向量遮罩寄存器） handling IF statements in vector code
Memory Banks （内存组） memory system optimizations to support vector processors
Stride （步幅） handling multi-dimensional arrays
Scatter-Gather （分散-集中） handling sparse matrices
Programming Vector Architectures （向量体系结构编程） program structures affecting performance
Question: how these optimizations map to MPI and OpenMP?

## Slide 34: 2. VLR and MVL: handling loops not equal to 32
VLR Vector Length Register; MVL  Max Vector Length
Vector length:
  Not known at compile time?
  Not multiple of 32?
Use strip mining for vectors over the maximum length:
/*find odd-size piece using modulo op % */
/*outer loop*/
/*runs for length VL*/
/*main operation*/
/*start of next vector*/
/*reset length to maximum vector length*/
low = 0; VL = (n % MVL);
for (j = 0; j <= (n/MVL); j=j+1) {
for (i = low; i < (low+VL); i=i+1)
Y[i] = a * X[i] + Y[i] ;
low = low + VL;
VL = MVL;
}
Vector Architectures
If n%MVL != 0, how to unroll loops?

## Slide 35: Optimizations
Multiple Lanes （多条车道） processing more than one element per clock cycle
Vector Length Registers （向量长度寄存器） handling non-32 wide vectors
Vector Mask Registers （向量遮罩寄存器） handling IF statements in vector code
Memory Banks （内存组） memory system optimizations to support vector processors
Stride （步幅） handling multi-dimensional arrays
Scatter-Gather （分散-集中） handling sparse matrices
Programming Vector Architectures （向量体系结构编程） program structures affecting performance
Question: how these optimizations map to MPI and OpenMP?

## Slide 36: 3. Vector mask registers
Handling IF statements in a loop
for (i = 0; i < 64; i=i+1) if (X[i] != 0)
X[i] = X[i] – Y[i];
If conversion use vector mask register to “disable/select” vector elements.
vsetdcfg 2*FP64 # Enable 2 64-bit FP vector regs
vsetpcfgi 1 # Enable 1 predicate register
vld v0,x5 # Load vector X into v0
vld v1,x6 # Load vector Y into v1
fmv.d.x f0,x0 # Put (FP) zero into f0
vpne p0,v0,f0 # Set p0(i) to 1 if v0(i)!=f0
vsub v0,v0,v1 # Subtract under vector mask
vst v0,x5 # Store the result in X
vdisable # Disable vector registers
vpdisable # Disable predicate registers
When the predicate register p0 is set, all following vector instructions operate only on the vector elements whose corresponding entries in the predicate register are 1.

## Slide 37: Masked Vector Instructions
C[4]
C[5]
C[1]
Write data port
A[7]
B[7]
P[3]=0
P[4]=1
P[5]=1
P[6]=0
P[2]=0
P[1]=1
P[0]=0
P[7]=1
Density-Time Implementation
  scan mask vector and only execute elements with non-zero masks
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
P[3]=0
P[4]=1
P[5]=1
P[6]=0
P[2]=0
P[1]=1
P[0]=0
Write data port
Write Disable
A[7]
B[7]
P[7]=1
Simple Implementation
  execute all N operations, turn off result writeback according to mask

## Slide 38: Optimizations
Multiple Lanes （多条车道） processing more than one element per clock cycle
Vector Length Registers （向量长度寄存器） handling non-32 wide vectors
Vector Mask Registers （向量遮罩寄存器） handling IF statements in vector code
Memory Banks （内存组） memory system optimizations to support vector processors
Stride （步幅） handling multi-dimensional arrays
Scatter-Gather （分散-集中） handling sparse matrices
Programming Vector Architectures （向量体系结构编程） program structures affecting performance
Question: how these optimizations map to MPI and OpenMP?

## Slide 39: 4. Memory banks
Memory system must be designed to support high bandwidth for vector loads and stores
  Memory start-up time: get the first word from memory in to a register
Spread accesses across multiple banks
  Control bank addresses independently
  Load or store non-sequential words
  Support multiple vector processors sharing the same memory
Example:
  32 processors, each generating 4 loads and 2 stores/cycle
  Processor cycle time is 2.167 ns, DRAM bank busy time (and bank latency) is 15 ns or about 67 M per second.
  How many minimum memory banks needed to allow all processors to run at the full memory bandwidth (no bank conflicts)?
    32 processors x 6 =192 memory accesses,
    15ns DRAM cycle /2.167ns processor cycle≈7 processor cycles
    7 x 192 1344!

## Slide 40: Memory Banks & Full Memory Bandwidth
No bank conflict is a critical condition for achieving full memory bandwidth.
192 requests
Cycle 1
192 requests
Cycle 2
192 requests
Cycle 3
192 requests
Cycle 4
192 requests
Cycle 5
192 requests
Cycle 6
192 requests*
Cycle 7
192 requests
Data transferred after bank busy time
Need at least 192x7 = 1344 banks without bank conflicts.
Assuming that requests are distributed as evenly as possible on banks.
Available banks 1344
(busy time 7 cycles)
Cycle 8
192 requests

## Slide 41
Example for bank conflict
192 requests
Cycle 1
128 requests
Cycle 2
192 requests
Cycle 3
192 requests
Cycle 4
192 requests
Cycle 5
192 requests
Cycle 6
192 requests *
Cycle 8
192 requests
Available banks 1280
(busy time 7 cycles)
Data transferred
Assuming total 1280 banks, and the dark gray memory only contains 128 banks, when coming into 192 requests, resulting in 64 bank conflicts.
64
128 requests
.
.
.
Cycle 9
Cycle 15
Waiting for
available banks
64 + 64 requests*
128*
192 requests
Cycle 7
(1)
(2)
(7)
(8)

## Slide 42: Theoretical Memory Bandwidth
DRAM clock frequency
Number of data transfers per clock: Two, in the case of "double data rate" (DDR, DDR2, DDR3, DDR4) memory.
Memory bus (interface) width: Each DDR, DDR2, or DDR3 memory interface is 64 bits wide. Those 64 bits are sometimes referred to as a "line."
Number of interfaces: Modern personal computers typically use two memory interfaces (dual-channel mode) for an effective 128-bit bus width.
For example, a computer with dual-channel memory and one DDR2-800 module per channel running at 400 MHz would have a theoretical maximum memory bandwidth of:
400,000,000 clocks per second × 2 transfers per clock × 64 bits per line × 2 interfaces = 102,400,000,000 (102.4 billion) bits per second (in bytes, 12,800 MB/s or 12.8 GB/s)

## Slide 43: Memory operations
Load/store operations move groups of data between registers and memory
Three types of addressing
  Unit stride
    Contiguous block of information in memory
    Fastest: always possible to optimize this
  Non-unit (constant) stride
    Harder to optimize memory system for all possible strides
    Prime number of data banks makes it easier to support different strides at full bandwidth
  Indexed (gather-scatter)
    Vector equivalent of register indirect
    Good for sparse arrays of data
    Increases number of programs that vectorize

## Slide 44: Memory Layout
Great for unit stride:
  Contiguous elements in different DRAMs
  Startup time for vector operation is latency of single read
What about non-unit stride?
  Above good for strides that are relatively prime to 8
  Bad for: 2, 4, 8 (worst)
  Better: prime number of banks…!
Vector Processor
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Addr
Mod 8
= 0
Addr
Mod 8
= 1
Addr
Mod 8
= 2
Addr
Mod 8
= 4
Addr
Mod 8
= 5
Addr
Mod 8
= 3
Addr
Mod 8
= 6
Addr
Mod 8
= 7

## Slide 45: Optimizations
Multiple Lanes （多条车道） processing more than one element per clock cycle
Vector Length Registers （向量长度寄存器） handling non-32 wide vectors
Vector Mask Registers （向量遮罩寄存器） handling IF statements in vector code
Memory Banks （内存组） memory system optimizations to support vector processors
Stride （步幅） handling multi-dimensional arrays
Scatter-Gather （分散-集中） handling sparse matrices
Programming Vector Architectures （向量体系结构编程） program structures affecting performance
Question: how these optimizations map to MPI and OpenMP?

## Slide 46: 5. Stride 跨步访问  multiple dimensional arrays
Technique to fetch vector elements that are not adjacent in memory
Stride  the distance between elements to be gathered in one register.
Example (Assume that the arrays are stored in row major order!!)
for (i = 0; i < 100; i=i+1) // A = B * D, 100*100 matrix
for (j = 0; j < 100; j=j+1) {
A[i][j] = 0.0;
for (k = 0; k < 100; k=k+1) A[i][j] = A[i][j] + B[i][k] * D[k][j];
}
Must vectorize multiplication of rows of B with columns of D
Use non-unit stride; D’s stride is 100 double words (800 bytes); B’s
stride is one double word (8 bytes)
Bank conflict (stall) occurs when the same bank is hit faster than bank busy time:
  #banks / GCD(stride, #banks) < bank busy time (in # of cycles)
Vector Architectures

## Slide 47: Stride example
Given
  8 memory banks, requests are sequentially sent to banks with a fixed time interval (e.g. one cycle)
  memory start-up latency of 12 cycles.
  bank busy time of 6 cycles
  bank busy time: the busy time is the time the bank is occupied with one request
Questions: How long will it take to complete a 64-element vector load
1. With a stride of 1?
2. With a stride of 32?
Answers:
1. Stride of 1: number of banks is greater than the bank busy time, so it takes 12 + 64 = 76 clock cycles  76/64 = 1.2 cycle for each vector element
2. Stride of 32: the worst case scenario happens when the stride value is a multiple of the number of banks, which this is! Every access to memory will collide with the previous one! Thus, the total time will be:
12 + 1 + 6 * 63 = 391 clock cycles 391/64 = 6.1 clock cycles per vector
element!
Vector Architectures

## Slide 48: How Multiple Banks Help, e.g. 8 banks
Start-up Mem latency, Stride 1
Bank conflicts
Start-up Mem latency, Stride 32
in the same bank
Bank busy time

## Slide 49: Optimizations
Multiple Lanes （多条车道） processing more than one element per clock cycle
Vector Length Registers （向量长度寄存器） handling non-32 wide vectors
Vector Mask Registers （向量遮罩寄存器） handling IF statements in vector code
Memory Banks （内存组） memory system optimizations to support vector processors
Stride （步幅） handling multi-dimensional arrays
Scatter-Gather （分散-集中） handling sparse matrices
Programming Vector Architectures （向量体系结构编程） program structures affecting performance
Question: how these optimizations map to MPI and OpenMP?

## Slide 50: 6 Scatter-gather
Support moving between compressed representation and normal representation of a sparse matrix or vector.
Consider sparse vectors A & C and vector indices K & M. A and C have the same number (n) of non-zeros:
for (i = 0; i < n; i=i+1)
A[K[i]] = A[K[i]] + C[M[i]];
x7, x5, x28 and x6 the starting addresses of vectors
Use index vector:
Vector Architectures
vsetdcfg 4*FP64 # 4 64b FP vector registers
vld v0, x7 # Load K[]
vldi v1, x5, v0) # Load A[K[]]
vld v2, x28 # Load M[]
vldi v3, x6, v2) # Load C[M[]]
vadd v1, v1, v3 # Add them
vsti v1, x5, v0) # Store A[K[]]
vdisable # Disable vector registers

## Slide 51: Optimizations
Multiple Lanes （多条车道） processing more than one element per clock cycle
Vector Length Registers （向量长度寄存器） handling non-32 wide vectors
Vector Mask Registers （向量遮罩寄存器） handling IF statements in vector code
Memory Banks （内存组） memory system optimizations to support vector processors
Stride （步幅） handling multi-dimensional arrays
Scatter-Gather （分散-集中） handling sparse matrices
Programming Vector Architectures （向量体系结构编程） program structures affecting performance
Question: how these optimizations map to MPI and OpenMP?

## Slide 52: 7 Programming vector architectures
Compilers can provide feedback to programmers
Programmers can provide hints to compiler
  https://software.intel.com/content/www/us/en/develop/articles/vectorization-with-the-intel-compilers-part-i.html
Vector Architectures
the percentage of operations executed in vector mode

## Slide 53: Summary of vector architecture
Optimizations:
  Multiple Lanes: > 1 element per clock cycle
  Vector Length Registers: Non-64 wide vectors
  Vector Mask Registers: IF statements in vector code
  Memory Banks: Memory system optimizations to support vector processors
  Stride: Multiple dimensional matrices
  Scatter-Gather: Sparse matrices
  Programming Vector Architectures: Program
structures affecting performance
Vector Architectures

## Slide 54: B. SIMD extensions for media apps
Media applications operate on data types narrower than the native word size.
  Graphics: 3x8-bit colors, 8-bit for transparency
  Audio: 8/16/24 bit/sample
Disconnect carry (进位) chains to “partition” adder.
  Example: a 256 adder can be partitioned to perform simultaneously:
    32 x 8-bit additions
    16 x 16-bit additions
    8 x 32-bit additions
    4 x 64-bit additions
Limitations, compared to vector instructions:
  Unlike vector machines with large register files e.g. the RV64V, thirty-two 64-bit elements in each of 32 vector registers
  Number of data operands encoded into op code
  No sophisticated addressing modes (strided, scatter-gather)
  No mask registers

## Slide 55: Intel SIMD extension to x86-64 implementations
Intel MMX (1996)
  Eight 8-bit integer ops or four 16-bit integer ops
Streaming SIMD Extensions: (SSE) (1999), SSE3 (2004),SSE4 (2007)
  Eight 16-bit integer ops
  Four 32-bit integer/fp ops or two 64-bit integer/fp ops
Advanced Vector Extensions (AVE) (2010)
  Four 64-bit integer/fp ops
Operands must be consecutive and at aligned memory locations
Generally designed to accelerate carefully written libraries rather
than for compilers.
Advantages over vector architecture:
  Cost little to add to the standard ALU
  Easy to implement
  Require little extra state  easy for context-switching
  Require little extra memory bandwidth
  No virtual memory problem of cross-page access and page-fault
SIMD Instruction Set Extensions for Multimedia

## Slide 57: Example: SIMD code for DXPY; Y = Y + a X
256 – bit SIMD multimedia instructions added to RISC-V.
.4D  instructions operating on 4 double precision operands at once.
SIMD Instruction Set Extensions for Multimedia
fld f0,a #Load scalar a
splat.4D f0,f0 #Make 4 copies of a
addi x28,x5,#256 #Last address to load
Loop: fld.4D f1,0(x5) #Load X[i] ... X[i+3]
fmul.4D f1,f1,f0 #a*X[i] ... A*X[i+3]
fld.4D f2,0(x6) #Load Y[i] ... Y[i+3]
fadd.4D f2,f2,f1 # a*X[i]+Y[i]...
# a*X[i+3]+Y[i+3]
fsd.4D f2,0(x6) #Store Y[i]... Y[i+3]
addi x5,x5,#32 #Increment index to X
addi x6,x6,#32 #Increment index to Y
bne x28,x5,Loop #Check if done

## Slide 58: Roofline performance model
c
Basic idea:
  Peak floating-point performance as a function of arithmetic intensity
  Ties together floating-point performance and memory performance
Arithmetic intensity (计算密度、计算访存比) Floating-point operations per byte read
Max Attainable GFLOPs/sec = Min (Peak Memory BW × Arithmetic Intensity, Peak Floating Point Performance)
Stream is a benchmark for memory performance
Dense matrix operations scale with problem size but sparse matrix operations do not!!

## Slide 59: Examples
Roofline: on the sloped portion of the roof the performance is limited by the memory bandwidth, on the flat portion it is limited by peak floating point performance
Mem BW
Mem BW
42.66/16.4=2.6
102.4/162=0.632
162*(1/8)=20.25
16.4*(1/8)=2.05

## Slide 60: C. Graphical Processing Unit - GPU
Given the hardware invested to do graphics well, how can it be supplemented to improve performance of a wider range of applications (General-purpose GPU)?
Basic idea:
  Heterogeneous execution model
    CPU is the host, GPU is the device
  Develop a C-like programming language for GPU
    Compute Unified Device Architecture (CUDA)
    OpenCL for vendor-independent language
  Unify all forms of GPU parallelism as CUDA thread
  Programming model: “Single Instruction Multiple Thread” (SIMT)
Graphical Processing Units

## Slide 61: Threads, blocks, and grid (CUDA terminology)
A CUDA thread is associated with each data element
  CUDA threads  thousands of threads are utilized to various styles of
parallelism: multithreading, SIMD, MIMD, ILP
CUDA threads with index are organized into thread blocks
  Thread Blocks: groups of up to 512 elements
  Executed on Multithreaded SIMD Processor: hardware that executes a whole thread block (32 elements executed per SIMD thread at a time)
Thread Blocks with index are organized into a grid
  Blocks are executed independently and in any order
  Different blocks cannot communicate directly but can coordinate using atomic memory operations in Global Memory
CUDA thread management handled by GPU hardware and CUDA runtime not by applications or OS
  A multiprocessor composed of multithreaded SIMD processors
  A Thread Block Scheduler (Hardware)

## Slide 62: NVIDIA GPU architecture
Similarities to vector machines:
  Works well with data-level parallel problems
  Scatter-gather transfers
  Mask registers
  Large register
Differences:
  No scalar processor
  Uses multithreading to hide memory latency
  Has many functional units, as opposed to a few deeply pipelined units like a vector processor

## Slide 63: Terms used in this chapter to official NVIDIA/CUDA
Graphical Processing Units
(SIMD Thread)
Academic
Industry

## Slide 64: Terms used in this chapter to official NVIDIA/CUDA
Graphical Processing Units

## Slide 65: Example: multiply two vectors of length 8192
C code version:
Graphical Processing Units
// Invoke DAXPY daxpy(n, 2.0, x, y); // DAXPY in C void daxpy(int n = 8192, double a, double *A, double *B, double *C) { for (int i = 0; i < n; ++i) A[i] = B[i] * C[i]; }
CUDA version:
It seems that we are programming on a CUDA thread at element level. (Abstraction: SIMT)
// Invoke DAXPY with 512 threads per Thread Block // code in C int nblocks = (n+ 511) / 512; daxpy<<<nblocks, 512 >>>(n, 2.0, A, B, C); // DAXPY in CUDA __global__ void daxpy (int n, double a, double *A,
double *B, double *C) { int i = blockIdx.x*blockDim.x + threadIdx.x; if (i < n)
A[i] = B[i] * C[i]; }
Q: Principle differences between C SIMD and CUDA SIMT?

## Slide 66: Example: multiply two vectors of length 8192
Grid  Code that works over all elements
Thread block analogous to a vector loop with a vector length of typically up to 512. Breaks down the vectorized loop into manageable set (warp) of 32 CUDA threads
32 elements (CUDA threads) per SIMD thread (Warp) x 16 SIMD threads=512 elements per thread block
 512 elements (CUDA threads) per thread block, SIMD instruction executes 32 elements at a time
Grid size = 8192 vector elements / 512 elements per block = 16 thread blocks
Thread block scheduler  assigns a thread block to a
multithreaded SIMD processor
Current-generation GPUs (Pascal P100) have 56 multithreaded SIMD processors (Streaming processors)
Graphical Processing Units

## Slide 67: Threads, blocks, and grid example
Graphical Processing Units
SIMD thread scheduler
Thread
block
scheduler
SIMD
Thread (Warp) 15

## Slide 68
A multithreaded SIMD processor has multiple SIMD lanes (L1-L16 in this example). The CUDA threads of the thread block are assigned to the lanes by the thread scheduler and are processed one at a time.
SIMD
SIMD
SIMD
32 vector elements map to
the term “warp” in CUDA
SIMD
Thread
SIMD
Thread

## Slide 69: Terms in CUDA Prog. Model vs GPU Architecture
CUDA Thread
CUDA
Thread
Block
CUDA
Warps
CUDA Grid contains 4 thread blocks
SIMD processor’s lane
split
Warps of a CUDA thread block can be viewed as SIMD threads in GPU architecture concurrently running on a SIMD processor and scheduled by SIMD thread scheduler.
Thread block scheduler
SIMD
processor
GPU
SIMD
Thread

## Slide 70: Threads, blocks, and grid example
SIMD thread scheduler (Warp scheduler)

## Slide 71
42
Figure 4.16 Scheduling of threads of SIMD instructions. The scheduler selects a ready thread of SIMD instructions and issues an instruction synchronously to all the SIMD Lanes executing the SIMD thread. Because threads of SIMD instructions are independent, the scheduler may select a different SIMD thread each time.

## Slide 72: NVIDIA GPU memory structures
Each SIMD Lane (CUDA Thread) has private section of off-chip DRAM
  “Private memory”, not shared by any other lanes (CUDA Thread)
  Contains stack frame, register spilling, and private variables that don’t fit in the registers.
  Recent GPUs cache this private memory in L1 and L2 caches
Each multithreaded SIMD processor also has local memory (Shared Memory) that is on-chip
  Shared by SIMD lanes / threads within a block only
  Latency is 100x lower than GPU Memory.
  Threads can access data in local memory loaded from global memory by other threads within the same thread block
The off-chip memory shared by SIMD processors is GPU
memory (Global memory)
  Host can read and write GPU memory
Graphical Processing Units
72

## Slide 73
55
Figure 4.18 GPU Memory structures.
GPU Memory (Global Memory) shared by all Grids (vectorized loops),
Local Memory (Shared Memory)  shared by all threads of SIMD instructions within a thread block (body of a vectorized loop).
Private Memory private to a single CUDA thread.
Notes: Not all variables are in use (or "live") at the same time, so, over the lifetime of a program, a given register may be used to hold different variables. However, two variables in use at the same time cannot be assigned to the same register without corrupting one of the variables. If there are not enough registers to hold all the variables, some variables may be moved to and from RAM. This process is called "spilling" the registers.[4] Over the lifetime of a program, a variable can be both spilled and stored in registers: this variable is then considered as "split".[5] Accessing RAM is significantly slower than accessing registers [6] and so a compiled program runs slower. Therefore, an optimizing compiler aims to assign as many variables to registers as possible. A high "Register pressure" is a technical term that means that more spills and reloads are needed; it is defined by Braun et al. as "the number of simultaneously live variables at an instruction".[7]
We call the on-chip memory that is local to each multithreaded SIMD Processor
local memory. It is a small scratchpad memory with low latency (a few dozen
clocks) and high bandwidth (128 bytes/clock) where the programmer can store
data that needs to be reused, either by the same thread or another thread in the same
Thread Block. Local memory is limited in size, typically to 48 KiB. It carries no
state between Thread Blocks executed on the same processor. It is shared by the
SIMD Lanes within a multithreaded SIMD Processor, but this memory is not
shared between multithreaded SIMD Processors. The multithreaded SIMD
Processor dynamically allocates portions of the local memory to a Thread Block
when it creates the Thread Block, and frees the memory when all the threads of the
Thread Block exit. That portion of local memory is private to that Thread Block.
Finally, we call the off-chip DRAM shared by the whole GPU and all Thread
Blocks GPU Memory. Our vector multiply example used only GPU Memory.
The system processor, called the host, can read or write GPU Memory. Local
memory is unavailable to the host, as it is private to each multithreaded SIMD
Processor. Private memories are unavailable to the host as well.

## Slide 74: Terminology (GPU hardware)
Threads of SIMD instructions
  Each has its own PC
  Thread scheduler uses scoreboard to dispatch
  No data dependencies between threads!
  Keeps track of up to e.g. 48 threads of SIMD instructions
    Hides memory latency
Thread block scheduler
  Schedule thread blocks to SIMD processors, each thread block is split to manageable sets (warps) (e.g. 32 CUDA threads / warp) and assigned to SIMD threads running on a SIMD processor.
Within each SIMD processor:
  16 or 32 SIMD lanes
  Wide and shallow compared to vector processors

## Slide 75: Example
NVIDIA GPU has 32,768 registers
  Divided into lanes
  A SIMD thread has up to:
    64 vector registers of 32 32-bit elements
    32 vector registers of 32 64-bit elements
Fermi has 16 physical SIMD lanes, each containing 2048 registers (2048 x 16 = 32,768)
Graphical Processing Units

## Slide 76
47
Figure 4.14 Simplified block diagram of a Multithreaded SIMD Processor with 16 SIMD lanes. The SIMD Thread Scheduler has, say, 48 independent threads of SIMD instructions that it schedules with a table of 48 PCs.
SIMD thread scheduler

## Slide 77: NVIDIA ISA -- PTX
48
PTX  Parallel Thread Execution
A PTX instruction describes the operation of a single CUDA thread!!
Like x86 instructions PTX instructions translate to an internal format
  X86  translation done by hardware at execution time
  PTX  translation done by software at compile time.
The format of a PTX instruction: opcode.type d,a,b,c
  d  destination operand
  a, b, c  source operands
Use virtual registers
NVIDIA act as co-processors. Similar to I/O units
Graphical Processing Units

## Slide 78: PTX arithmetic instructions
49

## Slide 79: PTX logical, memory access, and control flow

## Slide 80: Parallel Thread Execution (PTX) example
Graphical Processing Units
The following code is one CUDA thread, and 8192 of these created.
R8, blockIdx, 9 ; Thread Block ID * Block size (512 or 29)
shl.s32 add.s32
R8, R8, threadIdx ; R8 = i = my CUDA thread ID
ld.global.f64 RD0, [X+R8] ld.global.f64 RD2, [Y+R8]
mul.f64 RD0, RD0, RD4
add.f64 RD0, RD0, RD2
st.global.f64 [Y+R8], RD0
; RD0 = X[i]
; RD2 = Y[i]
; Product in RD0 = RD0 * RD4 (scalar a)
; Sum in RD0 = RD0 + RD2 (Y[i])
; Y[i] = sum (X[i]*a + Y[i])

## Slide 81: Conditional branching
GPU branch hardware uses:
  Internal mask registers
  Branch synchronization stack
    Entries consist of masks for each SIMD lane
    i.e. which threads commit their results (all threads execute)
  Instruction markers to manage when a branch diverges into multiple execution paths
    Push on divergent branch
  …and when paths converge
    Act as barriers
    Pops stack
Per-thread-lane 1-bit predicate register, specified by programmer
Graphical Processing Units
Notes: A GPU set predicate instruction (setp in Figure 4.17) evaluates the conditional
part of the IF statement. The PTX branch instruction then depends on that
predicate. If the PTX assembler generates predicated instructions with no GPU
branch instructions, it uses a per-lane predicate register to enable or disable each
SIMD Lane for each instruction. The SIMD instructions in the threads inside the
THEN part of the IF statement broadcast operations to all the SIMD Lanes. Those
lanes with the predicate set to 1 perform the operation and store the result, and the
other SIMD Lanes don’t perform an operation or store a result. For the ELSE
statement, the instructions use the complement of the predicate (relative to the
THEN statement), so the SIMD Lanes that were idle now perform the operation
and store the result while their formerly active siblings don’t. At the end of
the ELSE statement, the instructions are unpredicated so the original computation
can proceed. Thus, for equal length paths, an IF-THEN-ELSE operates at 50%
efficiency or less.
IF statements can be nested, thus the use of a stack, and the PTX assembler
typically generates a mix of predicated instructions and GPU branch and special
synchronization instructions for complex control flow. Note that deep nesting
can mean that most SIMD Lanes are idle during execution of nested conditional
statements. Thus, doubly nested IF statements with equal-length paths run at
25% efficiency, triply nested at 12.5% efficiency, and so on. The analogous
case would be a vector processor operating where only a few of the mask bits
are ones.

## Slide 82: Example
if (X[i] != 0)
X[i] = X[i] – Y[i];
else
X[i] = Z[i];
ld.global.f64 setp.neq.s32 @!P1, bra | RD0, [X+R8] P1, RD0, #0 ELSE1, *Push | ; RD0 = X[i] ; P1 is predicate register 1 ; Push old mask, set new mask bits
 |  | ; if P1 false, go to ELSE1
ld.global.f64 | RD2, [Y+R8] | ; RD2 = Y[i]
sub.f64 | RD0, RD0, RD2 | ; Difference in RD0
st.global.f64 | [X+R8], RD0 | ; X[i] = RD0
@P1, bra | ENDIF1, *Comp | ;bitwise complement mask bits
 |  | ; if P1 true, go to ENDIF1
ELSE1: | ld.global.f64 RD0, [Z+R8] | ; RD0 = Z[i]
 | st.global.f64 [X+R8], RD0 | ; X[i] = RD0
ENDIF1: <next instruction>, *Pop ; pop to restore old mask
Note: a thread has 64 vector components, each a 32 bit floating point
Graphical Processing Units
with *Push, *Comp, *Pop indicating
the branch synchronization markers inserted by the PTX assembler that push the old mask, complement the current mask, and pop to restore the old mask
Q. How the PTX codes are executed on GPU?
SIMT
Notes: Once again, normally all instructions in the IF-THEN-ELSE statement are executed
by a SIMD Processor. It’s just that only some of the SIMD Lanes are enabled
for the THEN instructions and some lanes for the ELSE instructions. As previously
mentioned, in the surprisingly common case that the individual lanes agree on the
predicated branch—such as branching on a parameter value that is the same for all
lanes so that all active mask bits are 0s or all are 1s—the branch skips the THEN
instructions or the ELSE instructions.
This flexibility makes it appear that an element has its own program counter;
however, in the slowest case, only one SIMD Lane could store its result every 2
clock cycles, with the rest idle. The analogous slowest case for vector architectures
is operating with only one mask bit set to 1. This flexibility can lead naive
GPU programmers to poor performance, but it can be helpful in the early stages
of program development. Keep in mind, however, that the only choice for a
SIMD Lane in a clock cycle is to perform the operation specified in the PTX
instruction or be idle; two SIMD Lanes cannot simultaneously execute different
instructions.

## Slide 83: Example
if (X[i] != 0)
X[i] = X[i] – Y[i];
else
X[i] = Z[i];
Graphical Processing Units
with *Push, *Comp, *Pop indicating
the branch synchronization markers inserted by the PTX assembler that push the old mask, complement the current mask, and pop to restore the old mask
Q. How the PTX codes are executed on GPU?
SIMT
1, 2, 3, 4, 5, 6, 7, 8
0, 0, 0, 0
1, 1, 1, 1, 1, 1, 1, 1 0, 0, 0, 0
1, 2, 3, 4, 5, 6, 7, 8
0, 0, 0, 0
0, 0, 0, 0, 0, 0, 0, 0 1, 1, 1, 1
1, 2, 3, 4, 5, 6, 7, 8
0, 0, 0, 0
3, 3, 3, 3, 3, 3, 3, 3
5, 4, 3, 9
True
False
Mask
X[ ]
X[ ]
Y[ ]
Z[ ]
Notes: Once again, normally all instructions in the IF-THEN-ELSE statement are executed
by a SIMD Processor. It’s just that only some of the SIMD Lanes are enabled
for the THEN instructions and some lanes for the ELSE instructions. As previously
mentioned, in the surprisingly common case that the individual lanes agree on the
predicated branch—such as branching on a parameter value that is the same for all
lanes so that all active mask bits are 0s or all are 1s—the branch skips the THEN
instructions or the ELSE instructions.
This flexibility makes it appear that an element has its own program counter;
however, in the slowest case, only one SIMD Lane could store its result every 2
clock cycles, with the rest idle. The analogous slowest case for vector architectures
is operating with only one mask bit set to 1. This flexibility can lead naive
GPU programmers to poor performance, but it can be helpful in the early stages
of program development. Keep in mind, however, that the only choice for a
SIMD Lane in a clock cycle is to perform the operation specified in the PTX
instruction or be idle; two SIMD Lanes cannot simultaneously execute different
instructions.

## Slide 84: Pascal architecture innovations
56
Each SIMD processor has
  Two SIMD thread schedulers, two instruction dispatch units
  Two sets of 16 SIMD lanes (SIMD instruction width=32, chime=2 cycles), 16 load-store units, 4 special function units
  Thus, two threads of SIMD instructions are scheduled every two clock cycles
Fast single-precision, double-precision, and half-precision floating-point arithmetic: The single precision floating-point is up to 10 TeraFLOP/s. Double-precision is at 5 TeraFLOP/s, and half-precision is about at 20 TeraFLOP/s when expressed as 2-element vectors.
High-bandwidth memory: Stacked, high-bandwidth memory (HBM2) has a wide bus with 4096 data wires running at 0.7 GHz offering a peak bandwidth of 732 GB/s, which is more than twice as fast as previous GPUs.
High-speed chip-to-chip interconnect: Pascal GP100 introduces the NVLink communication channel that supports data transfers of up to 20 GB/s in each direction.
Graphical Processing Units

## Slide 85
57
Figure 4.19 Block Diagram of Fermi’s Dual SIMD Thread Scheduler.
Compare this design to the single SIMD Thread Design in Figure 4.16.

## Slide 86: Pascal GPU
Graphical Processing Units

## Slide 87: NVIDIA Kepler Architecture

## Slide 89
60

## Slide 91: Loop-level parallelism
Focuses on determining whether data accesses in later iterations are dependent on data values produced in earlier iterations
  Loop-carried dependence
Example 1:
for (i=999; i>=0; i=i-1) x[i] = x[i] + s;
No loop-carried dependence
Detecting and Enhancing Loop-Level Parallelism

## Slide 92: Loop-level parallelism example 2
for (i=0; i<100; i=i+1) {
A[i+1] = A[i] + C[i]; /* S1 */ B[i+1] = B[i] + A[i+1]; /* S2 */
}
S1 and S2 use values computed by S1 in previous iteration
S2 uses value computed by S1 in same iteration
There are two different dependences:
1. S1 uses a value computed by S1 in an earlier iteration, because iteration i computes A[i+1], which is read in iteration i+1. The same is true of S2 for B[i] and B[i+1]. (loop-carried)
2. S2 uses the value A[i+1] computed by S1 in the same iteration. (no loop-carried)
Detecting and Enhancing Loop-Level Parallelism
Notes: There are two different dependences:
1. S1 uses a value computed by S1 in an earlier iteration, because iteration i computes
A[i+1], which is read in iteration i+1. The same is true of S2 for B[i] and
B[i+1].
2. S2 uses the value A[i+1] computed by S1 in the same iteration.
These two dependences are distinct and have different effects. To see how they
differ, let’s assume that only one of these dependences exists at a time. Because
the dependence of statement S1 is on an earlier iteration of S1, this dependence
is loop-carried. This dependence forces successive iterations of this loop to execute
in series.
The second dependence (S2 depending on S1) is within an iteration
and is not loop-carried. Thus, if this were the only dependence, multiple iterations
of the loop would execute in parallel, as long as each pair of statements
in an iteration were kept in order. We saw this type of dependence
in an example in Section 2.2, where unrolling could expose the parallelism.
These intra-loop dependences are common; for example, a sequence of vector
instructions that uses chaining exhibits exactly this sort of dependence.
It is also possible to have a loop-carried dependence that does not prevent
parallelism, as the next example shows.

## Slide 93: Loop-level parallelism example 3
for (i=0; i<100; i=i+1) {
A[i] = A[i] + B[i]; /* S1 */
B[i+1] = C[i] + D[i]; /* S2 */
}
S1 uses value computed by S2 in previous iteration but dependence
is not circular，neither statement depends on itself, and although S1 depends on S2, S2 does not depend on S1. A loop is parallel if it can be written without a cycle in the dependences because the absence of a cycle means that the dependences give a partial ordering on the statements. so loop is parallel. Transform to:
A[0] = A[0] + B[0];
for (i=0; i<99; i=i+1) { B[i+1] = C[i] + D[i];
A[i+1] = A[i+1] + B[i+1];
}
B[100] = C[99] + D[99];
Detecting and Enhancing Loop-Level Parallelism
Notes: Statement S1 uses the value assigned in the previous iteration by statement S2, so
there is a loop-carried dependence between S2 and S1. Despite this loop-carried
dependence, this loop can be made parallel. Unlike the earlier loop, this dependence
is not circular; neither statement depends on itself, and although S1 depends
on S2, S2 does not depend on S1. A loop is parallel if it can be written without a
cycle in the dependences because the absence of a cycle means that the dependences
give a partial ordering on the statements.
Although there are no circular dependences in the preceding loop, it must be
transformed to conform to the partial ordering and expose the parallelism. Two
observations are critical to this transformation:
1. There is no dependence from S1 to S2. If there were, then there would be a
cycle in the dependences and the loop would not be parallel. Because this other
dependence is absent, interchanging the two statements will not affect the execution
of S2.
2. On the first iteration of the loop, statement S2 depends on the value of B[0]
computed prior to initiating the loop.
These two observations allow us to replace the

## Slide 94: Loop-level parallelism examples 4 and 5
for (i=0;i<100;i=i+1) { A[i] = B[i] + C[i];
D[i] = A[i] * E[i];
}
No loop-carried dependence
for (i=1;i<100;i=i+1) { Y[i] = Y[i-1] + Y[i];
}
Loop-carried dependence in the form of recurrence
Detecting and Enhancing Loop-Level Parallelism

## Slide 95: Finding dependencies
Assume that a 1-D array index i is affine:
  a * i + b (with constants a and b)
An n-D array index is affine if it is affine in each dimension
Assume:
  Store to a * i + b, then
  Load from c * i + d
  i runs from m to n
  Dependence exists if:
    Given j, k such that m ≤ j ≤ n, m ≤ k ≤ n
    Store to a x j + b, load from c x k + d, and a * j + b = c * k + d
Detecting and Enhancing Loop-Level Parallelism

## Slide 96: Finding dependencies
Generally cannot determine at compile time
Test for absence of a dependence:
  GCD test:
    If a dependency exists, GCD(c,a) must evenly divide (d-b)
Example:
for (i=0; i<100; i=i+1) { X[2*i+3] = X[2*i] * 5.0;
}
Answer: a=2, b=3, c=2, d=0 GCD(c,a)=2, d-b=-3  no dependence possible.
Detecting and Enhancing Loop-Level Parallelism

## Slide 97: Reductions
Reduction Operation: for (i=9999; i>=0; i=i-1)
sum = sum + x[i] * y[i];
Transform to…
for (i=9999; i>=0; i=i-1) sum [i] = x[i] * y[i];
for (i=9999; i>=0; i=i-1)
finalsum = finalsum + sum[i];
Do on p processors:
for (i=999; i>=0; i=i-1)
finalsum[p] = finalsum[p] + sum[i+1000*p];
Note: assumes associativity!
Detecting and Enhancing Loop-Level Parallelism
For (i=0; i < p; i++)
finalsumall = finalsum[i] + finalsumall;

## Slide 98: Fallacies
GPUs suffer from being co-processors.
The I/O device nature of GPUs creates a level of indirection between the compiler and the hardware and gives more flexibility to GPU architects who can try new innovations and drop them if not successful. For example, the Fermi architecture changed the hardware instruction set without disturbing the NVIDIA software stack:
(1) from memory-oriented as x86 to register-oriented like RV64V;
(2) from 32-bit to 64-bit addressing
One can get good performance without providing good memory bandwidth.
Add more threads to improve performance.
If memory accesses of CUDA threads are scattered or not correlated the memory system will get progressively slower. The CUDA threads must enjoy locality of memory access.

## Slide 99: The DRAM Subsystem The Top Down View (Appendix A)

## Slide 100: Main Memory in the System
72
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 101: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column
72

## Slide 102: The DRAM subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”

## Slide 103: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM

## Slide 104: Breaking down a DIMM 双列直插内存模块
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 105: Ranks
Rank 0 (Front)
Rank 1 (Back)
Data <0:63>
CS<0:1>
(chip select)
Addr/Cmd
<0:63>
<0:63>
Memory channel

## Slide 106: Breaking down a Rank
Rank 0
<0:63>
Chip 0
Chip 1
Chip 7
. . .
<0:7>
<8:15>
<56:63>
Data <0:63>

## Slide 107: Breaking down a Chip
Chip 0
<0:7>
<0:7>
<0:7>
<0:7>
...
<0:7>

## Slide 108: Breaking down a Bank
<0:7>
row 0
row
16k-1
...
1B
2kB
1B (column)
1B
1B
...
<0:7>

## Slide 109: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column
80

## Slide 110: Example: Transferring a cache block
0xFFFF…F
0x40
...
64B
Physical memory space
Channel 0
DIMM 0
Rank 0
cache block
0x00

## Slide 111: Example: Transferring a cache block
0xFFFF…F
0x40
...
Physical memory space
Rank 0
Chip 0 Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
. . .
64B
cache block
Data <0:63>
0x00

## Slide 112: Example: Transferring a cache block
0xFFFF…F
0x40
...
Physical memory space
Rank 0
Chip 0 Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Row 0
Col 0
. . .
64B
cache block
Data <0:63>
0x00

## Slide 113: Example: Transferring a cache block
0xFFFF…F
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0 Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
8B
Data <0:63>
Row 0
Col 0
. . .
0x00
8B

## Slide 114: Example: Transferring a cache block
0xFFFF…F
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0 Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
8B
Data <0:63>
Row 0
Col 1
. . .
0x00

## Slide 115: Example: Transferring a cache block
0xFFFF…F
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0 Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
8B
8B
Data <0:63>
Row 0
Col 1
. . .
0x00
8B

## Slide 116: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0 Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
8B
8B
Data <0:63>
Row 0
Col 1
A 64B cache block takes 8 I/O cycles to transfer.
During the process, 8 columns are read sequentially.
. . .

## Slide 117: Latency Components: Basic DRAM Operation
CPU → controller transfer time
Controller latency
  Queuing & scheduling delay at the controller
  Access converted to basic commands
Controller → DRAM transfer time
DRAM bank busy time
  Simple CAS (column address strobe) if row is “open” OR
  RAS (row address strobe) + CAS if array precharged OR
  PRE + RAS + CAS (worst case)
DRAM → Controller transfer time
  Bus latency (BL)
Controller to CPU transfer time

## Slide 118: Multiple Banks (Interleaving) and Channels
Multiple banks
  Enable concurrent DRAM accesses
  Bits in address determine which bank an address resides in
Multiple independent channels serve the same purpose
  But they are even better because they have separate data buses
  Increased bus bandwidth
Enabling more concurrency requires reducing
  Bank conflicts
  Channel conflicts

## Slide 119: How Multiple Banks Help
Mem latency
Bank conflicts
Bank start-up latency
in the same bank
Bank busy time